Pre- and Coalescing Filters

How to Convert Float-type Drains to Air Pressure-operated Drains

- Remove bowls (make sure they are metal, not plastic – if plastic, call) from filters, disassemble float drains and pitch.

- Insert ½” sst bolt into hole – hex head with o-ring inside bowl. Secure with ½” nut from outside.

- Mount air chamber with Signal Converter somewhere nearby. Can be mounted in any position, anywhere - including fastened with tie-wraps to something. It’s not pretty but will work.

- Open Automatic TakeOff immediately above culvert and cut large blue hose – anywhere - (the one that makes TakeOff come off) and insert the large T-fitting. Run blue hose thru culvert, or wall or attic, to the ‘Signal Converter’. From there run two small hoses to the PT-100 pilots on drain.

- Drains will be open for about 3 seconds every time TakeOff comes off. Water will spit out of open port of PT-210   2-Way Valve.

- No real need to ever change timing, but can be done - call.

- ‘Signal Converter’ converts continues stream of blue air from TakeOff into momentary 3-secs pulse (reason why these valves are also called ‘Pulse Valves’).

Simple as that – call if you have questions.

Rolf