TechForAg LLC

Rolf Reisgies, General Manager

1855-A W. Davenport Street, Rhinelander, WI 54501

Flo’s Mobil 715-360-0108   Fax 715-362-7595   Rolf’s Mobil 715-360-3660

E-Mail Rolftfa@newnorth.net

Rebuilding TakeOff Air Controls

…that became waterlogged, because air drying system was neglected for some time.

If you are not familiar with Germania or Heritage air circuits, call and ask for the Self-Service DVD. No charge if you also buy the replacement parts from us.

There are (2) ways to go about this project – minimal rebuild and total rebuild. It’s one of those things. The minimal rebuild might do the trick. Worth trying on may be one or two units.

You may want to get a pair of Surgical Scissors, available from any medical supply house. Every midsize town has one…Great for temporarily pinching off air hoses.

A.	Minimal Rebuild:

Step 1: Check to make sure refrigerant drier is ‘on’ and working properly. . Cooling fins clean? Separation Bowl clean and empty? Actually spits water whenever you are using air?

Step 2: Replace filter elements of the Pre-Filter and the Coalescing Filter.

Step 3: Disconnect black hoses from PT-421 Main Valves, all of them one at a time. Turn air back on and let blow until you see no more ‘fog’ coming from any of the black hoses, takes a good minute. With that, the air supply system to the TakeOffs is clean and dry.

Step 4: Drain newly accumulated water, if any, from Pre-filter. Both filters should have automatic drains. Call us for details.

Step 5: Empty any water that may have accumulated in the 10-second timing chambers and the 2-min Start-up chambers. Remove from frame, remove fitting, turn upside down and shake.

Step 6: Replace the following:

(1) PT-421 Main Valve

(1) 34 AS or PT-110 Pilot - you may have either one.

(1) PT-100 Pilot at Start-Up Timer

(1) Whisker Valve at sensor

While the rest of the system will be wet, it’ll blow out by cycling the units a half dozen times.

B.	Complete Rebuild

Step 1 – 4 as above. Then replace:

For Start-up Timer:

(1) PT-100 pilot

(1) PT 210 2-way valve

(1) # 14 Flow Control

For Main Controls:

(1) PT-421

(1) 34AS or PT-110 pilot

(1) D Restrictor

(1) Whisker Valve

(2) Repair Kits for EV-125 at End-of-Milking Timer

We can supply all parts at reasonable cost. Call if you need more information. Likewise for the technician who’s actually going to work on the units.