Troubleshooting Heritage CIP Receiver Groups

- This Section Applies to All All TechForAg CIP Receiver Groups

Problem:

Milk Pump does not pump when you first start milking

Probable cause:

Pump is air locked. There’s an air leak either at the ball check valve or at the milk pump seal. Or anywhere else, downstream from the pump.

On newer installations, most likely it’s the ball of the check valve. On older installation it’s probably the milk pump seal. Good idea to change the seal kit every couple of years anyway.

99% chance on newer installations the ball is not sealing properly. Why not? Lousy quality balls.

Temporary Solution - fill the 4” milk filter with water right before you attach the machines to the first group of cows. The check valve now ‘leaks’ water – not air - past the ball and the pump will start just fine.

Permanent Solution – call for another ball. We’ll send you two or three of them. The balls that come with the check valve from the manufacturer are made of a hard plastic. If the surface is not perfectly ground, the valve will leak. Most of them are not. Manufacturer shrugs his shoulders.

We are working on a solution…

- This Section only pplies to CIP Groups controlled by the new Heritage Controller / Pipe Line Washer

Problem:

Controller goes thru normal cycle, but stops either at “Detergent Fill’ or at ‘Acid Fill’. Then

- Screen goes blank for a couple of seconds

- Then screen goes thru normal start-up sequence and self-test procedures (5 lines in very small print)

- Then once again shows ‘Detergent Fill’ (or ‘Acid Fill’) and stops

Probable cause:

Chemical Pump, either detergent or acid, has internal short. Short causes voltage draw-down, which causes Controller to shut and start up again.

Solution:

Replace chemical pump

___________________________________

Heritage Controller - Parts Replacement Procedure

PROFACE / SCREEN

Make sure POWER to system has been disconnected.

Disconnect keyed connections (Pug-ins) from Proface.

Remove Mounting Screws from Proface and  remove unit.

Install new (Programmed) Proface. Fasten in place.

Re-Connect keyed connections (Plug-ins) to New Proface.

POWER SUPPLY:

Make sure POWER to system has been disconnected.

Disconnect wires to Power Supply by loosening screw terminals.

Mark wires for reconnection to same terminals.

Remove Mounting Screws from Power Supply and remove unit.

Install new Power Supply. Fasten in place & Re-Connect wires to original locations.

CONTROL RELAYS: (Cage Clamp Technology – No Screw Terminals)

Make sure POWER to system has been disconnected.

Remove wires(With 0.5mm flat blade screw driver) and mark wires from terminals on Relays.

Remove entire Relay Assy. From Din Rail with flat blade screw driver at base of relay Assy.(Place tip in slot and push driver handle toward relay for release from Din.)

Clip in New Relay Assy. to original location. Replace wires by re-inserting to original terminal slots.

FUSES:

Same as Control Relays